Decibel Conversion: Power dB = 10 log [P2/P1] Decibels relative to Power Decibel Conversion: Voltage dB = 20 log [V1/V2] Decibels relative to Voltage across same resistance Decibel Conversion: Current dB = 20 log [I1/I2] Decibels relative to Current through same resistance Decibel Conversion: Milliwatts dBm = 10 log [Signal (mW)/1mW] Decibels relative to one milliwatt Decibel Conversion: Microvolts dBv = 20 log [Signal (V)/1V] Decibels relative to one microvolt across same resistance Decibel Conversion: Microamps dBA = 20 log [Signal (A)/1A] Decibels relative to one microamp through same resistance Power Conversion: dBw to dBm dBm = dBw + 30 Conversion from dBw to dBm. Voltage Conversion: dBv to dBv dBv = dBv + 120 Conversion from dBv to dBv. Voltage to Power Conversion: dBv to dBm dBm = dBv - 107 Where the constant 107 is as follows: * RF systems are matched to 50 P = V2 / R 10Log10[P] = 20Log10[V] - 10Log10[50] V = (PR)0.5 = 0.223 V = 223000 V For a resistance of 50and a power of 1 mW: 20Log10[223000V] = 107 dB Power Density dBw/M2 = 10Log10[V/M - A/M] Decibel-Watts per square meter. dBm/M2 = dBw/M2 + 30 Where the constant 30 is the decibel equivalent of the factor 1000 used to convert between W and mW: 10Log10[1000] = 30 Electric Field to Power Density dBm/M2 = dBV/M - 115.8 Where the constant 115.8 is as follows: P=¦E¦2/o Where o is the free space characteristic impedance (), equal to 120. Change this equation to decibels, converting dBW/M2 to dBmW/M2 for power density and dBV/M to dBV/M for the electric field. This yields 115.8 Electric Field Voltage V/M = 10{[(dBV/M) -120]/20} Electric Field Voltage in volts per meter Electric Field Current dBA/M = dBv/M - 51.5 Where the constant 51.5 is a conversion of the characteristic impedance of free space (120) into decibels: 20Log10[120] = 51.5 A/M = 10{[(dBA/M) -120]/20} Electric Field Current in amps per meter Antenna Factor AFdB = EdB - VrdB where: AF = Antenna Factor in dB/M E = Field strength at the antenna in dBµv/M Vr = Output voltage from receiving antenna in dBµv AF (for 50 ) = 20 log f (MHz) - G(dBi) - 29.78 dB. where f is the measured frequency (MHz), G is the antenna gain (dBi) over isotropic. (E) dBv/M = (Vo) dBv + (AF) dB/M AF is the antenna factor of the measuring antenna (as per calibration or per antenna manufacturer). E is the unknown or measured electric field strength. Vo is the adjusted (calibrated for cable & connector losses) spectrum analyzer output. Magnetic Flux Density dBpT = dBA/M + 2.0 Where the constant 2.0 is as follows: The magnetic flux density B is in Teslas (T) The permeability of the medium is in Henrys per meter (H/M) The permeability in free space is: o = 4 x 10-7 H/M Convert from T to pT and from A/M to A/M, and take the Log: 240 - 120 + 20Log10[4 x 10 -7] = 2.0 Conversion Units dB = decibels (Log10) m = milli = 10E-3  = micro = 10E-6 p = pico = 10E-12 dBw = decibels relative to one watt dBm = decibels relative to one milliwatt dBv = decibels relative to one volt dBv = decibels relative to one microvolt dBA = decibels relative to one microamp dBpT = decibels relative to one picoTesla V = Volts A = Amps I = Current R = Ohms (50) W = Watts P = Power H = Henrys T = Teslas AF = Antenna Factor M = Meter

BACK

http://www.radioing.com/eengineer/convert.html